## Slide 1: Guidesheet for the Design of Land Treatment Systems Utilized at Wineries
The intent:
Ensure the discharge of winery wastewater is conducted in a manner which:
will not cause contamination of the water resources of the State of Michigan;
b) will be protective of the environment and public health;
will not cause the development of nuisance conditions due to odors or unsightly appearances.
Provides general information regarding the design of land treatment systems to meet the needs of individual wineries.

## Slide 2
All wineries discharging their wastewater to the groundwater through land application should apply for a groundwater discharge authorization.
If an authorization is required, the type of authorization will be based upon the information provided on the permit application and the requirements of the Part 22 Rules.

## Slide 3
Overview of Land Treatment of Winery Wastewater
Wastewater typically receives minimal treatment prior to discharge.
Rely on land treatment to meet groundwater quality standards
Method of Land Treatment: Slow rate, Overland flow, Rapid infiltration, Subsurface Soil Absorption
Methods of Wastewater Distribution: Spray Irrigation, Vented Pipe, Subsurface Tile, Truck Mounted Applicator, Drip Irrigation, etc.
The choice of methods of Land Treatment and Wastewater Distribution are left to the facility.

## Slide 4
Factors to consider include:
Financial Resources Staffing Requirements
Expertise Required Proximity of Suitable / Available Land
Site characteristics Ownership of the Site
Characteristics of the Wastewater Potential Odor Issues
Density and proximity of residential dwellings, schools, and/or commercial operations (restaurants, childcare, eldercare)
Wastewater Flows (Current and Future)

## Slide 5
Land treatment systems are expected to be designed, constructed, and operated with the intent to protect the water resources of the State of Michigan and the public health.
The DEQ reserves its authority under Part 31 of the NREPA to evaluate proposed and existing systems and require any and all changes and or additions the DEQ deems necessary and appropriate to ensure the protection of the waters of the State and public health.

## Slide 6
Methods of Land Treatment
(brief descriptions)
Slow Rate: Application of wastewater to a vegetated land surface with the applied wastewater being treated as it flows through the plant and soil matrix.
Distribution typically accomplished through spray or drip irrigation technology; however, other technologies or approaches such as distribution from a vehicle mounted apparatus may be acceptable.
Overland Flow: Application of wastewater to the upper reaches of vegetated slopes with excess wastewater collected at the end of the slopes for reapplication.
To function properly, overland flow systems require slowly permeable soils to facilitate the distribution of the wastewater.

## Slide 7
Rapid Infiltration: Discharge to basins constructed in areas with highly permeable soils. The applied wastewater receives minimal treatment as it percolates through the soil matrix to the groundwater.
The use of this method will require site specific pretreatment of the wastewater prior to discharge.
Subsurface Soil Absorption (Drain field): Discharge through a distribution system placed below ground level.
Suitability is a function of the soil properties of the site and the extent to which the winery utilizes materials such as bentonite and diatomaceous earth.
Preventing such substances and others from entering and clogging the subsurface distribution system is critical.
The use of this method may require site specific pretreatment of the wastewater prior to discharge.

## Slide 8
Dry-wells
The DEQ does not recommend the use of dry-wells.
Generally not suitable for the discharge wastewater of this nature.
Concerns with the elevated Biochemical Oxygen Demand (BOD) of the wastewater and the potential to solubilize naturally occurring heavy metals within the soil column.
Those facilities currently using dry-wells are encouraged to begin exploring alternative methods for managing their wastewater.
The DEQ intends to phase out the use of dry-wells by wineries and will be working with facilities through the permit application process to accomplish this goal.

## Slide 9
Land Treatment Design
Proper design of a land treatment system requires a number of parameters to be determined and/or evaluated.
Maximum Daily Discharge Volume (MDDV) crush and non-crush operations
Maximum Annual Discharge Volume (MADV),
Wastewater Characteristics Soil Characteristics
Hydraulic Loading Rates Constituent loading rates
Proper Sizing of the Land Treatment System

## Slide 10
Maximum Daily Discharge Volume (MDDV)
Critical to decisions regarding:
Authorization Type (323.2211, 323.2210, 323.2216, or 323.2218)
Selection and Design of the Land Treatment System.
The most accurate method: Flow meter, installed to measure the volume of wastewater discharged.
A second method: Flow meter and/or run-time meter installed on pumps used to bring water into the facility.
The assumption being that the volume of water coming into the facility is equal to the volume being discharged (Not as accurate but still reliable).
The DEQ recommends the use of reliable, properly installed and calibrated flow meters for measuring and monitoring wastewater discharge flows.

## Slide 11
Estimated MDDV
Theoretically possible to estimate the MDDV.
The DEQ does not recommend using estimates of MDDV.
Inaccurate estimates could lead to miscalculations of a number of
critical elements of the system.
If actual flow data cannot be obtained the Guidesheet provides two methods for estimating MDDV.

## Slide 12
Napa Valley formula:
MDDV = (Annual Production (gallons) X 1.5)/Number of Crush Days
Concerns:
Formula only calculates the average volume during “crush season”
Not an estimation of the maximum daily volume.
Appears to assume all fruit is processed at the winery. (may or may not be true).
Some facilities have indicated the Napa Valley formula appears to provide a fairly accurate estimate based on their historical data.

## Slide 13
Alternative approach:
Suggested by an expert from the Michigan wine making industry.
Referred to (with permission) as the “Fenn Valley Method.”
Considers wastewater produced during both “crush” as well “non-crush” periods.
The greater of the two estimated volumes is considered the MDDV.

## Slide 14
MDDV during the “crush”:
Based on the maximum number of tons the facility can physically handle per day.
Assumed to be a fixed characteristic which cannot change without structural modifications, additional equipment, increases in staffing, and significant capital expenditure.
Assumes:
One ton of grapes = 150 gallons of juice
1.4 gallons of water is used per gallon of grape juice
MDDV(crush) (gallons) =
Processing Capacity (tons)/day X 150 gallons juice/ton X 1.4 gallons water used/gallon of juice

## Slide 15
MDDV for “non-crush”
Based on the number of fermentation tanks and their volume(s) that can be emptied and cleaned on a given day
Assumes 0.15 gallons of water is used per gallon of fermenter capacity
MDDV(non-crush) (gallons) = (Volume “A(t)” + Volume “B(t)” + Volume “C(t)” + ……) X 0.15
Where;
Volume “A(t)” = Number of volume “A” fermenters X volume “A” (gallons)
Volume “B(t)” = Number of volume “B” fermenters X volume “B” (gallons)
Volume “C(t)” = Number of volume “C” fermenters X volume “C” (gallons)

## Slide 16
Concerns:
Based on assumptions which will not hold true for all facilities.
Actual volume generated could be significantly different from the estimates calculated using this approach.
In General
Land treatment system = significant investment of time and $
As such, use caution when using estimated MDDV calculated from any method.

## Slide 17
Maximum Annual Discharge Volume (MADV)
DEQ recommends the use of flow meters for determining MADV.
Alternatively:
Information from California and Oregon indicate the unit volume ratio of wastewater generated to wine produced appears to range from 2.9:1 to 8:1.
Michigan wine producers contacted indicated this range appears to be fairly reliable.
The ratio that would apply to a particular facility is a function of water use practices implemented by the wine maker.

## Slide 18
Wastewater Characteristics
 |  | Typical Winery Wastewater * |  | Michigan Data | Typical Domestic Wastewater **
Parameter | Units | Crush | Non-Crush | Not Specified | Residential
Total Phosphorus | mg/L | 1 - 10 | 1 - 40 | 1.2 - 22 | 6 - 12
Total Inorganic Nitrogen | mg/L | 1 - 40 | 1 - 40 | 0.53 - 69 | 4 - 13
Sodium | mg/L | 35 - 200 | 35 - 200 | 3.2 - 380 | -
pH | S.U. | 2.5 - 9.5 | 3.5 - 11 | 5.01 - 6.56 | -
BOD5 | mg/L | 500 - 12,000 | 300 - 3,500 | 550 - 4,300 | 155 - 286
 |  |  | Wineries |  |  | 
Parameter | Units | A | B | C | D | E
Total Phosphorus | mg/L | 8.62 | 1.29 | 5.82 | 9.19 | 1.72
Total Inorganic Nitrogen | mg/L | 4.44 | 3.64 | 18.5 | 8.77 | 2.63
Sodium | mg/L | 396 | 792 | 53 | 124 | 28
Chloride | mg/L | 673 | 1,500 | 10.8 | 53 | 7.2
pH | S.U. | 5.8 | 6.7 | 5.5 | 6 | 6.8
BOD5 | mg/L | 2,249 | 336 | 3,578 | 3,111 | 957

## Slide 19
In the absence of facility specific wastewater quality data, the MDEQ recommends using the default values listed in Table 2.
Parameter | Units | Default Values
Total Phosphorus | mg/L | 40
Total Inorganic Nitrogen | g/L | 69
Sodium | mg/L | 400
Chloride | mg/L | 500
pH | S.U. | 2.5 - 11
BOD5 | mg/L | 12,000
* Default values = Average + 1 Std Dev
The DEQ recommends winery wastewater be analyzed for the following:
BOD5 Total Kjeldahl Nitrogen
Ammonia Nitrogen (NH3 – N) Total Phosphorus
Nitrate Nitrogen (NO3- - N) Sodium
Nitrite Nitrogen (NO2- - N) Chloride
pH
Parameter | Units | Average Concentration | Standard Deviation | Default Value*
Total Phosphorus | mg/L | 5.26 | 4.61 | 9.87
Total Inorganic Nitrogen | mg/L | 7.6 | 9.5 | 17.1
Sodium | mg/L | 279 | 300 | 579
Chloride | mg/L | 459 | 612 | 1071
pH | S.U. | 6.13 | 0.9 | 7.03
BOD5 | mg/L | 2,046 | 1,768 | 3,814

## Slide 20
Biochemical Oxygen Demand and Constituent Loading Rates
Available information indicates winery wastewater, can and will contain very high concentrations of BOD.
Groundwater monitoring data from sites utilized by food processors around the State indicate impacts from wastewater discharges resulting in high BOD loading rates.
The specific impacts are heavy metals such as iron, manganese, arsenic, and lead

## Slide 21
Caused by:
Development of anaerobic conditions within the soil.
A result of oxygen being consumed by aerobic organisms metabolizing organic substrate which comprise the BOD in wastewater.
Once oxygen is no longer available, organic substrates are metabolized by anaerobic organisms.
The metabolic activity of these organisms and the environmental conditions produced by their activity results in the chemical reduction of naturally occurring heavy metals in the soil.
Once reduced, the metals become water soluble, thus mobile and eventually leach into the groundwater.

## Slide 22
The Part 22 Rules do not specify a limit for BOD in wastewater or groundwater
DEQ recommends limiting the concentration of BOD in effluents to 30 mg/l prior to discharge.
For wastewaters with BOD concentrations above 30 mg/l, the DEQ recommends limiting daily BOD loading rates to land treatment systems to 50 pounds per acre.
Based on the results of a study conducted at Michigan State University.
Facilities proposing BOD loading rates above 50 LBS/acre/day will be required to demonstrate the approach does not result in contamination of the groundwater resource.

## Slide 23
The following equation may be used to calculate the estimated maximum daily quantity (in pounds) of a constituent, such as BOD discharged based on a known or assumed maximum concentration of the constituent and the MDDV:
(MDDV gallons/1,000,000) X Constituent mg/L X 8.34 = LBs constituent
Example
The quantity of BOD discharged from a facility with a MDDV of 700 gallons with a BOD concentration of 12,000 mg/L is:
(700 gallons/1,000,000) X 12,000 mg/L X 8.34 = 70 LBs BOD

## Slide 24
Site Soil Characteristics
The DEQ anticipates most wineries will want to use soil information published by the USDA, Natural Resources Conservation Service (NRCS) in their design calculations.
If the soil beneath the point of discharge has been excavated, replaced, or modified, published information may no longer apply and on-site testing may be necessary.
When published information regarding soil permeability is utilized for calculating hydraulic loading rates, and it is given as a range of expected values, use seven percent of the minimum value given the most restrictive soil layer within the solum (0 ‑ 60 inches typically) as required by Part 22 Rules [R 323.2233(4)(a)(v)].

## Slide 25
Example
Published data for a proposed site indicates the most restrictive soil layer occurs at a depth between 12 and 18 inches and has a permeability that ranges from 1.0 – 4.0 inches/hour (in/hr). The maximum daily hydraulic loading rate for this site would be:
1.0 X .07 X 24 = 1.68 acre-inches/day (in/d)
0ne acre-inch equates to 27,150 gallons distributed over one acre or approximately 0.6 gallon/square-foot (one acre = ~43,560 square feet). Thus, the soil at this site is hydraulically suited to receive up to 45,612 gallons per acre per day (~1.0 gallon per square foot per day).

## Slide 26
Sizing of Land Treatment Systems
Size will be a function of the information and calculations discussed earlier.
It is important to use maximum daily values rather than averages in the basis of design.
Using average values will likely result in frequent overloads and thus inadequate treatment.
Negative impacts to the groundwater and potential downgradient users of the resource.

## Slide 27
Discharge Management
The soil environment provides a variety of mechanisms by which winery wastewater may be treated.
For these mechanisms to function as needed, the wastewater must be applied in a controlled manner.
Land treatment systems are expected to be managed to maintain aerobic conditions within the soil and allow time between applications for soil organisms to aerobically metabolize organic constituents in the wastewater.
In general, the lower the loading rate and longer the period between applications the better.